## Slide 1: The Network Services Interface
An Overview of the NSI Framework and the GLIF Automated GOLE dynamic network provisioning demonstration at
Supercomputing 2011

## Slide 2: NSI Framework
The “NSI Framework” is an OGF standard:
  It specifies an abstract model of a network “Connection”
  It specifies an abstract “Topology” model over which Connections are established
  It specifies an abstract “Network Service Agent” (NSA) that represents each network service region.
  It specifies a high level protocol model between NSAs to enable inter-domain NSI Services.
The NSI Framework is technology agnostic
  The NSI architecture does not expect or require specific transport technologies in the underlying infrastructure.
  It is therefore suitable for multi-layer, multi-protocol, multi-service data transport environments.
  It is secure by design, giving each agent full authority over their local processes and policies with explicit - but service specific - authorization performed at each service boundary for all inter-domain requests.

## Slide 3: Why NSI? Why now?
Emerging applications require predictable and deterministic network resources. Connection oriented services can meet these needs.
In a global environment, these services must be automated in order to scale, and must be inter-domain in order to provide the reach required of global science, and they must be secure to be globally practical.
Much work has been done to develop effective protocols for automated provisioning, … but these protocols have been experimental, and/or do not address the larger architectural aspects of a global environment.
And existing approaches are rarely interoperable – resulting in limited and isolated islands of functionality.
NSI leverages much this prior work and experience to define an inter-domain architecture and a provisioning standard that is technology agnostic, secure, and globally scalable.
The NSI Framework and protocol(s) are the product of an open and community-wide process within the Open Grid Forum.
The result is a consensus standard that meets a wide range of needs…and is widely understood and widely supported, and will therefore be widely deployed in networks and widely adopted by applications.

## Slide 4: A Basic Overview of NSI Architecture
NSI protocol
A
E
C
D
D
E
Domain C
Domain B
B
A
Requesting
Agent (RA)
Network Resource Manager
Provider
Agent (PA)
NRM
Network Services Interfae
NSA
Network Services Agent
NSA

## Slide 5: The Network Service Agent
A Network Service Agent is associated with every NSI Network domain:
  It acts as Provider Agent (PA) when receiving service requests for other NSAs (peer networks or user clients)
  It can act as a Requesting Agent (RA) to farm out portions of the resource management to other NSAs (networks)
  It interacts with an independent Network Resource Manager (NRM) to allocate and reserve network resources within its own network domain

## Slide 6: NSI Connection Service
The NSI Connection Service (NSI-CS) is the first protocol defined under the NSI Framework
  NSI-CS specifies a set of basic primitives and functional capabilities that create and manage a NSI Connection through its life cycle.
NSI-CS Features:
  Supports Reserve, Provision, Release, Terminate, and Query primitives.
  Supports conventional “chain” signaling but also incorporates novel “tree” signaling - providing greater flexibility and control to the Requesting Agent – i.e. the user.
  Allows users to schedule connections in advance.
  Allows service providers to define common service specifications to aid in end to end service interoperability

## Slide 7: Basic NSI Topology Model
Bonaire
Aruba
P0
X0
P1
L1
X1
P0
P2
P1
P2
P0
X0
P1
L1
X1
P1
P2
P0
P2
P4
P5
Bonaire
Aruba
The NSI model assigns ownership of all physical components to one network or the other.
Conventional physical infrastructure –
Networks, switches, ports, and links
The physical topology is translated to a derivative “resource graph” consisting of resources, and stitching relations
Technology agnostic inter-domain Service Termination Points (“STP”s) are defined and mapped logically to internal physical components. External relations are NSI Service Demarcation Points (“SDP”s).
Bonaire
Aruba
Bonaire:B1
Aruba:A0
Aruba:A1
Bonaire:B0
STP
Bonaire:B2
STP
Aruba:A2
SDP
By hiding all internal structure and only exposing inter-domain STPs and their peering SDP relations, we arrive at the basic NSI Topology Model of networks, STPs, and the SDPs that indicate inter-domain adjacency.
P1
X1
P0
P2
P0
X0
P1
P2
Bonaire
Aruba
L1
B1
A0
A1
B0
B2
A2
P5
P4

## Slide 8: How NSI-CS Works…
RM
RM
NSA
RM
NSA
NSA
NSA
Appl
RA
PA
The user application

## Slide 9: Anatomy of a Connection
The User (RA) specifies connection constraints (ostensibly externally measurable) for the access portion of the service instance
The Network (PA) decides how to fulfil those constraints across the transport section.
Ingress
Service Termination Point
“A”
Egress
Service Termination Point
“Z”
Transport section
Access section
Access section
Egress Framing
Transport framing
Ingress Framing

## Slide 10: Network Service Agent Request processing path
PA
1
2
3
4
5
6
1
2
3
4
5
6
RA
PA
PA
A
B
C
D
M
B
C
D
A
B
C
D
Chain model
Tree model
A
Z
A
Z
A
Z
1
2
3
4
5
6
3rd party request

## Slide 11: Mixed model request handling Request processing path using mixed model
RA
3
4
5
6
1
2
A
B
C
D
7
8
Chain model
Tree model
Chain model
Tree model

## Slide 12: NSI Connection Service Protocol Exchange
This is the life cycle msg sequence between the NSI Connection Service (PA) and the requester (RA) for a normal successful connection request.
PA
RA
scheduled
reserve
request
reserve
complete
idle
reserve
Setup
Complete
Release
Request
Release
Complete
idle
In Service
Released
reserve
scheduled
“Start” TIme
init
In Service
Released
idle
“Duration” TImer
“Setup” TIme
setup
request

## Slide 13: The GLIF Automated GOLE Pilot Project

## Slide 14: The Automated GOLE Fabric
USLHCnet
PSNC
JGN-X
MANLAN
NetherLight
Cern
UvA
CzechLight
KRLight
AIST
KDDI Labs
StarLight
ESnet
Cal Tech
GLORIAD
GEANT
ACE
Nordunet
The Global Lambda Integrated Facility (GLIF)
  The GLIF Automated GOLE Pilot was initiated in 2010 to provide a global fabric of Open Lightpath Exchanges for the express purpose of maturing the dynamic provisioning software, demonstrating the value of GOLEs to emerging network service models, and to develop a set of BCP for these services.

## Slide 15: The NSI Demo at SC2011
The Playground

## Slide 16: NSI Software Implementations:
OpenNSA – NORDUnet (Copenhagen, DK)
DRAC – SURFnet (Amsterdam, NL)
AutoBAHN – GEANT (Poznan, PL)
G-LAMBDA-A - AIST (Tsukuba, JP)
G-LAMBDA-K – KDDI Labs (Fujimino, JP)
DynamicKL – KISTI (Daejeon, KR)
OSCARS – ESnet (Berkeley, US)

## Slide 17: Watch it Live!
Visualization
Java web start thing: http://163.220.30.174:8070/monitor.jnlp
Google earth plugin: http://kote-ps-1.ps.jgn-x.jp/ps/autoearth-nsi/
Google earth kml: http://kote-ps-1.ps.jgn-x.jp/ps/autoearth-nsiAutoMAP.kml

## Slide 18: NSI Development & Road Map
OGF NSI-CS version 1.0 is in final draft now
Demos:
  Sep 2011: First NSI CS Interop Plugfest – GLIF 2011 Rio de Janeiro, BR
  Oct 2011: First NSI Transport Provisioning Future Internet Assembly 2011 Poznan, PL
  Nov 2011: Global NSI + AutoGOLE Demonstration Supercomputing 2011 Seattle, US
Futures:
  NSI Topology – dynamic distributed topology exchange. Required to automated the local maintenance of local topology and to enable scalable global pathfinding.
  NSI Performance Verification – An architecture for automated service verification and fault localization/remediation
  Common Service Definitions – Enabling interoperable transport services

## Slide 19: Key Endorsements
NSI is gaining very broad support.
I once made a connection thiiiiiis long using NSI CS v1.0

## Slide 20: OGF NSI Working Group
The OGF NSI WG is an Open working group
This means if *you* have ideas you would like to see incorporated into the NSI framework and/or protocols, please get active in the process:
    Contact one of the active WG members and pick their brain
    Join the mailing list, lurk and get up to speed, then join the calls…
    Contribute – ask, comment, propose…help us sort thru the issues to achieve clarity within the group and consensus within the broader community
Thank You!