## Slide 1: IDCP and NSI: Lessons Learned, Deployments and Gap Analysis
Chin Guok, Inder Monga
OGF 34
Oxford, UK

## Slide 2: Outline
IDCP protocol background
Deployment
Status
What have we learnt?
Moving from IDCP to NSI

## Slide 3: Background on IDCP
IDCP: Inter-Domain Control Protocol
Specified by a focused group
Protocol specification shared openly
  IDC Specification: http://www.controlplane.net
  OGF Document: http://www.ggf.org/documents/GFD.170.pdf
A point-to-point connection service
  Service layer (web-services)
  Multi-domain
  Reservation and Scheduling
  Detailed features presented later in the presentation
OSCARS implementation/documentation: http://www.es.net/services/virtual-circuits-oscars/

## Slide 4: History of IDCP in relationship to OSCARS
OSCARS v0.6 RC1 released (Dec 2011)
OSCARS v0.6 is field tested in SCinet (SC11), and ESnet ANI 100G prototype network (Nov 2011)
OSCARS interops with OGF NSI protocol v1 using an adapter at NSI Plugfest at GLIF Rio, participants include OpenDRAC (SURFnet), OpenNSA(NORDUnet), OSCARS(ESnet), G-lamdba (AIST), G-lambda (KDDI Labs), AutoBAHN (GÉANT project), and dynamicKL (KISTI) (Sep 2011)
OSCARS v0.6 SDK released allowing researchers to build and test PCEs within a flexible path computation framework (Jan 2011)
2004 2005 2006 2007 2008 2009 2010 2011
Funded as a DOE project (Aug 2004)
First production use of OSCARS circuit to reroute LHC Service Challenge traffic due to transatlantic fiber cut (Apr 2005)
Collaboration with Internet2 BRUW project (Feb 2005)
First dynamic Layer-3 interdomain VC between ESnet (OSCARS) and Internet2 (BRUW) (Apr 2006)
Formulation of DICE (DANTE, Internet2, CANARIE, ESnet) Control Plane WG (Mar 2006)
Collaboration with GÉANT AMPS project (Mar 2006)
Successful Layer-2 reservation between ESnet (OSCARS) and GÉANT2 (AutoBAHN), and Nortel (DRAC) (Nov 2007)
First dynamic Layer-2 interdomain VC between ESnet (OSCARS) and Internet2 (HOPI) (Oct 2007)
First ESnet Layer-2 VC configured by OSCARS (Aug 2007)
Adoption of OGF NMWG topology schema in consensus with DICE Control Plane WG (May 2007)
Successful control plane interop between OSCARS and g-Lambda using GLIF GNI-API GUSI (GLIF Unified Service Interface) (Dec 2008)
DICE Inter-Domain Controller (IDC) Protocol v1.0 specification completed (May 2008)
NSI WG started in OGF
First use of OSCARS by SCinet (SC09) to manage bandwidth challenges (Nov 2009)
Successful control and data plane interop between OSCARS, g-Lambda and Harmony using GLIF GNI-API Fenius (Nov 2009)
Draft architecture design for OSCARS v0.6 (Jan 2009)
DICE IDCP v1.1 released to support brokered notification (Feb 2010)

## Slide 5: Multiple interoperable implementations for IDCP
OSCARS open-source software
  Internet2 DCN service software (OSCARS + DRAGON)
  Internet2 ION service software (OSCARS)
Internet2’s OS3E + NDDI software (OpenFlow + IDCP)
AutoBAHN (GEANT, other NRENS)
GENI Stitching Framework (GENI Aggregate Manager + IDCP)

## Slide 6: IDCP Global Deployment WAN, Regional, Campus, Testbeds, Researchers
IDCP
US:
13 Deployed
26 in progress
50 universities by end of 2012/13
200 locations with GENI by end of 2014
RNP
GEANT
KOREN
JGN2
Notes: Across pacific and atlantic

## Slide 7: IDCP Features in a nutshell
IDCP Features | Comments
Primary mode of operation is Chain | Tree mode possible but not implemented operationally. Chain is a reduced form of a tree
Signaling starts at the IDCP edge domain | Third party signaling from arbitrary disconnected domain is not supported. Is that a prime requirement or nice to have?
Error handling along the chain | Error messages are propagated up and down the chain. Easy to roll-back
Path information carried in the message | Other than path benefits, easy to implement circuit monitoring, reporting, visualization etc.
Technology parameters range supported | Allows for quicker negotiation, and less complex topology updates
Management functions incorporated | ListReservations and queryReservations (security built in, policies out of scope)

## Slide 8: IDCP features in a nutshell (contd.)
IDCP Features | Comments
Notification mechanism specified | For errors or for third party management systems or for service composition
Topology Query supported (multi-domain) | In NMWG format.
Optional constraints | Environment to test out new features. Has led to rich relationships with researchers and projects. The following extensions to IDCP have been done but not standardized * multi-layer path-finding Topology in, Topology out Anycast Protection/survivability

## Slide 9: Learnings
Multi-domain failure debugging is not trivial
  Simpler model the better
  Error notifications need to be as explicit as possible
  Management functions in the protocol (subject to AA)
Topology service essential, does not have to be complex
  Leverage the perfSONAR service
  Do not duplicate repositories that people are already keeping
Vision is a composition of network services
  Security is important
  So is access to schedules, circuit identification
  Proliferation of dynamic state is tough to manage

## Slide 10: Learnings contd.
Chain mode makes it easier for negotiation across domains
  Yay/Nay are simple constructs, but won’t scale
  User wants to know what exactly failed
  User does not always want to specify exact parameters
Simple client interface and library help integration with various middleware
  Think of the web-page and AJAX
  Client should not be state, topology or process heavy
Service interoperability across network is more complex than the protocol
  Operational procedures and security policies differ in every network
  Protocol specification is not enough

## Slide 11: Top Considerations for NSI 2.0
Production Considerations for Connection Services | NSI CS v1.1 Capability | Notes
Reservation with specific bandwidth, start time, and duration |  | Implemented in NSI CS v1.1
Asynchronous Communications between requester and provider |  | Implemented in NSI CS v1.1
Common profiles for authentication and trust |  | Initial requirements have been established (e.g. trust between PA/RA), but implementation is under consideration
Notification to third-party applications/services (e.g. circuit monitoring, resource coordination/reporting) |  | Under consideration for NSI CS v2.0
Topology publication and distribution |  | Under discussions for NSI CS v2.0
Ability to specify path information for reservation used by end user or NOC to traffic engineer path |  | Under consideration for NSI CS v2.0
Lightweight client for applications/middleware |  | Under discussions for NSI CS v2.0

## Slide 12: Questions?

## Slide 13: Moving from IDCP to NSI
The “INERTIA” danger
GENI is deploying network stitching soon
  Cannot derail them for a year/NSI 2.0
Flag day is not an option with so many deployments
  Will require two to live side by side?
Other considerations
  Let’s ensure perfSONAR does not break with the new topology model
    400 deployments worldwide
    What is the impact if you break it?
    Who is going to invest the resources?
    Network engineers are using it now!

## Slide 14: Summary
IDCP is gaining deployment
NSI has a great list of features, approach and flexibility, but base features still not at par with IDCP
Need to simplify, focus and crank out NSI 2.0 for wider adoption
Cross over will take time, cannot have a flag day

## Slide 15: IDCP (OSCARS view only)
Currently deployed in 21 networks including wide-area backbones, regional networks, exchange points, local-area networks, and testbeds.
Under consideration for an additional 26 green field deployments in 2012
Deployments using OSCARS v0.6 above dotted line